## Slide 1: Lecture 07: GEOSPATIAL VISUALIZATION
March 16, 2021
CSC/SDS 235
Visual Analytics
portions of this lecture adapted from NCSU MEA582 Lecture Notes by Helena Mitasova

## Slide 2: Data Challenge 2: Coordinated Views

## Slide 3: Outline
Geospatial data representations
Visualization techniques
Challenges
Guidelines for making good geoviz

## Slide 4: Geospatial data (def.)
Geospatial data represents features / objects in space
(usually relative to their position on the surface of the Earth)

## Slide 5: Remote sensing: satellite
Sensors:
Data:
SRTM
LANDSAT
Geospatial Analysis and Modeling MEA592 – Helena Mitasova

## Slide 6: Remote sensing: airborne
Sensors:
Data: x,y,z points 1 point per 0.3m
Orthophotography 0.15m resolution
Geospatial Analysis and Modeling MEA592 – Helena Mitasova

## Slide 7: Ground-based sampling
Ground based imagery
Google Street view
Equipment: RTK GPS, Sonar, laser scanner, ISCO sampler
Geospatial Analysis and Modeling MEA592 – Helena Mitasova

## Slide 8: Two kinds of geospatial information
Discrete
  lines, points or areas (e.g. roads, streams, census blocks, land use)
  each object has a distinct position
Geospatial Analysis and Modeling MEA592 – Helena Mitasova

## Slide 9: Two kinds of geospatial information
Discrete
  lines, points or areas (e.g. roads, streams, census blocks, land use)
  each object has a distinct position
Continuous
  a function defined over space w=f(x,y)
  each point in space has a distinct value, and the change between two neighbouring values is usually small (elevation, precipitation)
Geospatial Analysis and Modeling MEA592 – Helena Mitasova

## Slide 10: Geospatial data models
Geospatial Analysis and Modeling MEA592 – Helena Mitasova
Two ways to project georeferenced data into discrete GIS (global information system) representations:
raster
(surface = regular grid)
vector
(feature = point, line, area w/position)

## Slide 11
Geospatial data models: raster
continuous: elevation, precipitation discrete: land use, roads
3 herbaceous
Geospatial Analysis and Modeling MEA592 – Helena Mitasova
5 developed
1 water

## Slide 12: Geospatial data models: vector
continuous: isolines, distribution discrete: streets, streams, census blocks
Geospatial Analysis and Modeling MEA592 – Helena Mitasova

## Slide 13: Geographic visualization
Most common: maps
Useful for making geospatial comparisons

## Slide 14: Geographic visualization: points

## Slide 15: Geographic visualization: glyphs

## Slide 16: Geographic visualization: over time

## Slide 17: Geographic visualization: filled regions

## Slide 18: Geographic visualization: heatmaps

## Slide 19: Geographic visualization: connections

## Slide 20: Examples: NYT maps

## Slide 21: Discussion
Question:
What makes geographic visualizations so compelling?

## Slide 22: Challenge 1: flat earth?

## Slide 23: Impact of map projections
Deetz, C. H., & Adams, O. S. (1921). Elements of map projection with applications to map and chart construction.
Campbell, J.E., & Shin, M. (2012). Geographic Information System Basics.

## Slide 24: Challenge 2: granularity mismatch
Image courtesy of politicalmaps.org

## Slide 25: Example: 2012 US Presidential Election
Image courtesy of politicalmaps.org

## Slide 26: Example: 2012 US Presidential Election
Image courtesy of politicalmaps.org

## Slide 27: Challenge 3: perceptual trickery
Flashback to when we talked about perception
What preattentive features are at work in these maps?
color (hue)
clustering (proximity)
size

## Slide 28: Example: 2012 US Presidential Election
Image courtesy of http://politicalmaps.org

## Slide 29: Example: 2012 US Presidential Election
Number of Electoral Votes Captured
OBAMA
332
ROMNEY
206
270 votes
needed to win

## Slide 30: Challenge 4: non-adjacent comparison
Image courtesy of http://politicalmaps.org
Are Maine and
S. California voting similarly?

## Slide 31: Challenge 5: missing data
Image courtesy of http://politicalmaps.org

## Slide 32: Challenge 6: occlusion
What’s going on in Turkmenistan and Uzbekistan?

## Slide 33: Discussion: (rough) guidelines for maps
Question:
What do we need to keep in mind
to make good geographic visualizations?

## Slide 34
Demo
making interactive maps with

## Slide 35: Data Challenge 3: Spatiotemporal Data

## Slide 36: Up next
Thursday: network / graph data
Guest speaker!